## Slide 1: Pollution
PowerPoint presentation 1.1
Unit 101: Introduction to the Built Environment
Unit 301: Understanding construction practice in Wales

## Slide 2: Pollution
An important goal of any project should be to maintain or improve the quality of life.
It is essential that the natural environment is seen as a vital part of this quality of life.
Designers and constructors must therefore look in detail at the effects their projects and the materials being used in those projects are having on the environment.

## Slide 3: Landfill
The problem is that Britain produces 25 million tonnes of rubbish every year. This presents a tremendous disposal problem.
Some local authorities incinerate their rubbish. This yields energy which can be used to make small amounts of electricity. The residue is separated into ash, which is buried and metal which is recycled.
Unfortunately, all too often the rubbish is simply buried in landfill sites.
These are large holes that are usually the result of the extraction of resources such as clay or gravel. The material gradually rots and, as this happens, produces gases.

## Slide 4: Landfill
There is a scarcity of building land in many areas, and this has led to the development of many former landfill sites.
Unfortunately, the gases can migrate up through the soil and collect in the buildings.
This leads to a great risk of explosion.
Even buildings hundreds of miles from the landfill site can be affected because the gases can move horizontally.

## Slide 5: Landfill
The two most important gases are:
“carbon dioxide” (35%), which suffocates
and
“methane” (65%) which can explode.

## Slide 6: Landfill
The Solution
Sealing the floors and lower sides of the houses with a special membrane will prevent gases from entering the building.
In addition, if a space or layer of granular material is placed underneath the floor slab, this will allow the gases to be vented into the atmosphere.
In the case of buildings next to landfill sites, the answer is to dig a metre wide vent trench along the side of the landfill and fill it with stones of about 50 mm diameter.

## Slide 7: Landfill
The trench, which must be at least as deep as the landfill, is sealed with a membrane barrier on the side furthest away from the landfill to prevent horizontal movement.
The gas is then released into the atmosphere through vent pipes.
The composition of the gas is regularly monitored.
The ground conditions which result from landfill normally require piles to be driven into the soil to provide a firm foundation for construction.
By careful treatment of the situation, the construction industry is able to provide both homes and industrial units which are safe from landfill gasses.