## Slide 1: PowerPoint 5: Safe systems of work
PowerPoint presentation 1.1
Unit 101: Introduction to the Built Environment
Unit 304: Conform to general workplace health, safety and welfare

## Slide 2: PowerPoint 5: Safe systems of work
1. Health and safety in construction
1.5 Development of safe systems of work

## Slide 3: Objectives
By the end of the session, learners will be able to:
  explain how safe systems of work are developed and used
  describe the implications of not having safe systems of work in place
  complete risk assessments, method statements and COSHH assessments
  explain how to apply Construction Design and Management (CDM)
  describe the requirements for site signage
  outline the different levels of the Construction Skills Certification Scheme (CSCS).

## Slide 4: Safe systems
A safe system of work is a procedure to eliminate the risks that are involved in a specific operation. The priority of a safe system of work is to eliminate any risks involved.
Following a risk assessment process can reduce risks on site and ensure safe systems of work.
It is vital that safe systems and practices are adhered to so that everyone is working to the same high safety standards at all times.
Without these systems in place, accidents might occur that could cause injury or death.

## Slide 5: Risk assessment
A risk assessment needs to be completed:
  to back up the manufacturer’s data sheet for the Control of Substances Hazardous to Health (COSHH) Regulations
  to assess various activities carried out by employees.
  As a construction worker, you must assess the risk to yourself and others when work is being carried out. This is at the heart of working safety.
After a risk assessment has been completed it will, as a minimum, result in the use of personal protective equipment (PPE) and the presence of a first-aid kit. However, the more risk that is identified in the risk assessment, the more mitigation processes need to be put in place to protect the operative and anyone else that may be affected by the work being completed.

## Slide 6: Risk assessment
There are five steps to a risk assessment:
Look for hazards.
Decide who or what may be harmed.
Evaluate the risks and take suitable precautions.
Record your findings.
Review and revise these finding regularly.
The Management of Health and Safety at Work Regulations 1999 legally require employers to make decisions about the hazards, significant or not, faced in the workplace.

## Slide 7: Risk assessment
Key definitions
Accident: an unplanned, undesired occurrence which may result in harm or loss.
Hazard: anything that has the potential to cause loss or harm.
Risk: how likely it is that a hazard will actually cause harm or loss.
When a risk assessment is put together, you have to identify the work hazard and calculate the likelihood of an accident happening. Therefore, identifying the risk rating is important.

## Slide 8: Risk assessment
Risk rating
Value of likelihood X Value of consequence
No likelihood 0 No injury or loss 0
Very unlikely 1 First aid 1
Unlikely 2 Up to 3 days off work 2
Likely 3 Over 3 days off work 3
Very likely 4 Major injury 4
Certainty 5 Fatality 5
Ratings and assessments will be expected by the HSE during an inspection and are also needed by insurance companies in the event of a claim.

## Slide 9: Risk assessment: document example

## Slide 10: Method statements
A method statement or safety procedure document is part of a workplace’s safety plan.
It is mainly used in construction to describe a document giving specific instructions on how to safely perform a work-related task, or operate equipment.
It is written after the risk assessment has been undertaken.
Method Statement

## Slide 11: Permit to work
According to the HSE:
‘… Where proposed work is identified as having a high risk, strict controls are required. The work must be carried out against previously agreed safety procedures, a “permit-to-work” system.
The permit-to-work is a documented procedure that authorises certain people to carry out specific work within a specified time frame. It sets out the precautions required to complete the work safely, based on a risk assessment. It describes what work will be done and how it will be done; the latter can be detailed in a method statement.
The permit-to-work requires declarations from the people authorising the work and carrying out the work.’
  Permits to work - COSHH (hse.gov.uk)

## Slide 12: Permit to work
Examples of where a permit to work is required are:
  completing ‘hot works’, eg welding
  working in confined spaces, eg, in a loft
  lone working, eg, in a sewer
  maintaining machinery and equipment, eg, maintenance of a disc cutter etc.

## Slide 13: COSHH
COSSH stands for Control of Substances Hazardous to Health.
These regulations were introduced to control exposure to hazardous substances. The regulations detail the safety requirements for working with the following materials:
  solids, eg soda crystals
  liquids – eg bleach
  dust – eg drilling through asbestos ceilings
  fumes – eg when soldering
  vapours – eg when solvent-cementing waste pipes
  gases – eg flammable gases.

## Slide 14: COSHH
Before using any substance you must check the COSHH data sheet and:
  conduct a risk assessment prior to use
  take precautions to minimise risk to health (eg establish if harm is caused by ingestion, inhalation or absorption)
  invoke control measures to minimise risk further
  regularly monitor levels of use and exposure to the risk
  receive training and information on the use of the substance including substituting a hazardous substance with a less harmful alternative.

## Slide 15: COSHH
Remember: some domestic items can be hazardous, eg loft insulation can be an irritant to the skin.
Domestic cleaning chemicals that are either acid or alkali can be corrosive and burn the skin.
The rule is that for any item with a COSHH you need to wear gloves to protect your hands.

## Slide 16: Company management system
A company management system is a set of tools for planning and implementing policies, practices, guidelines, processes and procedures.
These tools are used in the development, deployment and execution of the company’s plans, strategies, forecasts and associated management activities to ensure that a company complies with all regulatory requirements.

## Slide 17: CDM
Roles in a project
  The principal designer (PD) is responsible for all the pre-construction phase planning and design work.
  The principal contractor (PC) must manage and coordinate the construction side of the project.
  The contractor (C) must plan and manage the work under their control, liaise with the PC and carry out the works without compromising health and safety.
  More information on the CDM Regulations 2015 can be found here: trusted-traders-guidance-for-businesses-434474.pdf (which.co.uk)

## Slide 18: CDM Regulations
The Construction (Design and Management) (CDM) Regulations 2015 are intended to ensure health and safety issues are properly considered and any risk minimised.
The regulations set out definitions for principal designers, principal contractors and contractors.

## Slide 19: Site safety signs
Construction sites can be dangerous places, with hazards lurking around every corner. Construction site safety signs are designed to reduce the risk of accidents and injuries, protecting workers and members of the public.
As well as pointing out hazards and directing site users to medical equipment for use in emergencies, building site signs also play a crucial role in the efficient day-to-day running of the construction site.
Employers have a legal responsibility to ensure that every site has the relevant construction signage. This is an essential step to reduce the incidence of workplace accidents and injuries and ensure that members of the public are aware of the location of prohibited areas.

## Slide 20: CSCS
A Construction Skills Certification Scheme (CSCS) card proves that an individual has passed a health and safety test which enables them to work on a building site.
The cards come in different colours which are in line with the level of qualifications held by the individual.
  Green – construction site operative/labourer.
  Gold – skilled worker (NVQ Level 3 qualified).
  Black – senior manager (NVQ Level 4 qualified).
  Red – trainee/apprentice.
  White – individual with a construction-related job (eg cleaning of sites).

## Slide 21
Any questions?