## Slide 1: PowerPoint 2 : Understand how to follow procedures.
PowerPoint presentation 1.1
Unit 101: Introduction to the Built Environment
Unit 305: Conform to productive work practices.

## Slide 2
Learners will need to consider the following when answering worksheets for this topic:-
How organisational procedures are applied to plan and carry out productive work.
How to maintain documentation in accordance with organisational procedures.
How to contribute to zero/low carbon outcomes in the built environment.

## Slide 3
General site paperwork
No building site could function properly without a certain amount of paperwork. Below are listed the more common types of site paperwork used daily.
Timesheet
Timesheets record hours worked and are completed by every employee individually. Some timesheets are basic, asking just for a brief description of the work done each hour, but some can be complicated. In some cases, timesheets may be used to work out how many hours the client will be charged for.
Day worksheets
Day worksheets are often confused with timesheets but are different as they are used when there is no price or estimate for the work, to enable the contractor to charge for the work. Day worksheets record work done, hours worked and sometimes materials used.

## Slide 4
Job sheet
A job sheet is like a day worksheet, it records work done but is used when the work has already been priced. Job sheets enable the worker to see what needs to be done and the site agent or working foreman to see what has been completed.
Variation order
This sheet is used by the architect to make any changes to the original plans, including omissions, alterations and extra work.
Confirmation notice
This is a sheet given to the contractor to confirm any changes made in the variation order, so that the contractor can go ahead and carry out the work.
Orders/requisitions
A requisition form or order is used to order materials or components from a supplier.

## Slide 5
Delivery notes
Delivery notes are given to the contractor by the supplier, and list all the materials and components being delivered. Each delivery note should be checked for accuracy against the order (to ensure what is being delivered is what was asked for) and against the delivery itself (to make sure that the delivery matches the delivery note). If there are any discrepancies or if the delivery is of a poor quality or damaged, you must write on the delivery note what is wrong before signing it and ensure the site agent is informed so that he/she can rectify the problem.
Invoices
Invoices come from a variety of sources such as suppliers or subcontractors, and state what has been provided and how much the contractor will be charged for it.

## Slide 6
Delivery records
Delivery records list all deliveries over a certain period (usually a month), and are sent to the contractor’s Head Office so that payment can be made
Daily report/ site diary
This is used to pass general information (deliveries, attendance etc.) on to a company’s Head Office.
Accident and near miss reports
It is a legal requirement that a company has an accident book, in which reports of all accidents must be made. Reports must also be made when an accident nearly happened but did not in the end occur – known as a ‘near miss’. It is everyone’s responsibility to complete the accident book. If you are also in a supervisory position, you will have the responsibility to ensure all requirements for accident reporting are met.

## Slide 7
Drawings
Drawings are done by the architect and are used to pass on the client’s wishes to the building contractor. Drawings are usually done to scale because it would be impossible to draw a full-sized version of the project. A common scale is 1:10, which means that a line 10 mm long on the drawing represents 100 mm in real life. Drawings often contain symbols instead of written words to get the maximum amount of information across without cluttering the page.
Specifications
Specifications accompany a drawing and give you the sizes that are not available on the drawing, as well as telling you the type of material to be used and the quality that the work must be finished to.
Schedules
A schedule is a list of repeated design information used on big building sites when there are several types of similar room or house. For example, a schedule will tell you what type of door must be used and where. Another form of schedule used on building sites contains a detailed list of dates by which work must be carried out and materials delivered etc.

## Slide 8
Work programme
A work programme is a method of showing very easily what work is being carried out on a building and when. The most common form of work programme is a bar chart. Used by many site agents or supervisors, a bar chart lists the tasks that need to be done down the left side and shows a timeline across the top. A work programme is used to make sure that the relevant trade is on site at the correct time and that materials are delivered when needed. A site agent or supervisor can quickly tell from looking at the chart if work is keeping to schedule or falling behind.
Bar charts
The bar or Gantt chart is the most popular work programme as it is simple to construct and easy to understand. Bar charts have tasks listed in a vertical column on the left and a horizontal timescale running along the top.
Each task is given a proposed time, which is shaded in along the horizontal timescale. Timescales often overlap as one task often overlaps another.

## Slide 9
The bar chart can then be used to check progress. Often the actual time taken for a task is shaded in underneath the proposed time (in a different way or colour to avoid confusion). This shows how what has been done matches up to what should have been done. A bar chart can help you plan when to order materials or plant, see what trade is due in and when, and so on. A bar chart can also tell you if you are behind on a job; if you have a penalty clause written into your contract, this information is vital.
When creating a bar chart, you should build in some extra time to allow for things such as bad weather, labour shortages, delivery problems or illness. It is also advisable to have contingency plans to help solve or avoid problems, such as:
• capacity to work overtime to catch up time • bonus scheme to increase productivity • penalty clause on suppliers to try to avoid late or poor deliveries • source of extra labour (for example from another site) if needed. Good planning, with contingency plans in place, should allow a job to run smoothly and finish on time, leading to the contractor making a profit.

## Slide 11
Critical paths
A critical path can be used in the same way
as a bar chart as it can show what
needs to be done and in what sequence.
A critical path also shows a timescale
but differently to a bar chart. The timescale
on a critical path shows minimum
amount of time and maximum amount of time.
The critical path is shown by a series of circles called event nodes. Each node is
split into three, with the top third showing the event number, the bottom left
showing the earliest start time and the bottom third the latest start time.
Notes: You can see that the nodes are joined together by lines, which represent the tasks carried out in between the event nodes. The length of task should be relevant to the times written in the lower 2/3rds of the nodes.
The more information on a critical path, the harder it is to read. Some critical paths have the information on each task written underneath the lines between the nodes, which make it easier to read.

## Slide 12
An example of a critical path
Notes: The tutor can use the text explaining nodes 0–5 from page 51 and 52 of Carpentry and Joinery Level 3.

## Slide 13
Reducing carbon emissions in buildings will be critical to achieving net zero emissions by 2050;
Efficient, zero carbon buildings take advantage of available, cost-effective technology to reduce emissions while increasing health, equity and economic prosperity in local communities.
Reducing carbon emissions in buildings will be critical to achieving the Paris climate goals and achieving net zero emissions by 2050.
Buildings represent 39% of global greenhouse gas emissions, including 28% in operational emissions and 11% in building materials and construction.
Global building floorspace is projected to double by 2060 and only 3% of investment in new construction is green and efficient, locking in high emissions for decades.
The renovation rate for existing buildings is barely 1%, less than a third of the rate needed to meet the Paris climate goals.

## Slide 14
While the decarbonization challenges for buildings are significant, so are the opportunities. Efficient, zero carbon buildings take advantage of available, cost-effective technology to reduce emissions while increasing health, equity and economic prosperity in local communities.
There are four crucial trends driving zero carbon buildings:
decarbonization,
electrification,
efficiency
digitalization.
These four good “DEEDS” work in combination to reduce the carbon emissions and overall cost of building operations and supporting infrastructure. Buildings can achieve zero carbon (or zero carbon ready) performance by eliminating fossil fuel use for heating, using on-site and/or off-site renewable energy, reducing the use of high global warming potential refrigerants and using low-carbon, reused or recycled materials in construction.

## Slide 16
Any questions?