## Slide 1: PowerPoint 2: Understand safe working practices
PowerPoint presentation 1.1
Unit 101: Introduction to the Built Environment
Unit 306: Move handle and store resources

## Slide 2: Objectives
By the end of this session you will be able to:
Identify the legislation in relation to safe handling of materials and equipment
State the importance of manual handling
State the importance of using lifting aids when handling materials and equipment

## Slide 3: Safe Handling of Materials And Equipment
The Manual Handling Operations Regulations 2002 places the following duties on employers and employees:

## Slide 4: Safe Handling of Materials And Equipment
 | Employees duties
1 | Employees are responsible for complying with the safe systems of work enforced by their employer
2 | Use the equipment provided by the employer
3 | Report hazards encountered
4 | Make sure that their activities do not endanger others

## Slide 5: Manual Handling
What is Manual Handling?
The definition of manual handling: The transportation or movement of a load (including person, animal or object) from one place to another by lifting, handling, pushing, pulling or bodily force.
FACTS
Lifting and moving loads manually is one of the most common causes of injury at work.
56,000 Work Related MSD cases in construction per year
There is no truly ‘safe’ weight limit for manual handling operations so try to find alternatives.

## Slide 6: Manual Handling
When you must manually handle loads consider: TILE
Task - how often, how much twisting or bending is needed?
Individual capability, male or female, old or young, experienced or inexperienced?
Load - how heavy? Good grip? Bulky? Heavier at one end?
Environment - hot, cold, uneven floor, windy, stairs?

## Slide 7: Manual Handling
Kinetic lifting
The correct posture before lifting
The correct techniques when lifting
When lowering a load you must adopt the correct posture and technique
See activity sheet 15 on the step by step guide to lifting correctly
The most common injury when lifting incorrectly is Spinal Injury

## Slide 8: The use of lifting aids when handling materials and equipment
Lifting Gear There are numerous items of small lifting equipment available to assist with handling materials on site and in the workshop. Only use these if you are qualified to use them.

## Slide 9
Most bricks delivered to sites are prepacked and banded, using either plastic or metal bands to stop the bricks from separating until ready for use.
Why are bricks and blocks stacked on pallets?
Bricks and blocks

## Slide 10
Aggregates are normally delivered in tipper lorries, although nowadays one-tonne bags are available and can be handled by crane.
How can aggregates be protected from contamination?
Storing aggregates

## Slide 11
Wood and sheet materials
Carcassing timber, joinery grade wood, hardwoods, plywood, other sheet materials and joinery components all have specific storage requirements.
What problems can occur from poor storage of timber and sheet materials?

## Slide 12
Ironmongery includes not just fittings and fixtures made of iron, but also hardware made from brass, chrome, porcelain and glass.
How should ironmongery be stored?
Ironmongery

## Slide 13
Because of their chemical nature, there are risks if adhesives are not stored, used and handled correctly.
What regulations govern the storage of adhesives?
Adhesives

## Slide 14
Drainage pipes
Drainage pipes are
made from vitrified
clay or plastic. Clay
pipes are easily
broken, and any
pipes can roll.
How are drainage
pipes best stored?

## Slide 15
Aggregates can be supplied as bagged materials, as can cement and plaster.
What are the main requirements of a storage shed?
Bagged materials

## Slide 16
Oil-based,
water-based and powdered paint products all need to be stored differently to make sure they remain useable.
Why do paints need to be stored in
date order?
Paints

## Slide 17
Temperature, access and general cleanliness are important when storing decorative papers and decorating tools.
Why are wallpapers stored in batches?
Decorative papers and decorating tools

## Slide 18
Highly flammable liquids include: Liquefied Petroleum Gas, petrol, cellulose thinners, methylated spirits, chlorinated rubber paint and white spirit.
What are the main requirements for storing highly flammable liquids?
Highly flammable liquids

## Slide 19
If only a small number of sheets of glass are to be stored, they can be leant against a stable surface, as shown.
What are the storage requirements for glass?
Glass