## Slide 1: Materials
PowerPoint presentation 1.1
Unit 101: Introduction to the Built Environment
Unit 306: Conform to general workplace health, safety and welfare

## Slide 2: Materials
Materials are required to be brought on site, unloaded, stored or fixed directly into the building. The storage provided will depend on the nature of the material and its relative value.
The positioning of materials in relation to their final position must be considered.
Costs can be saved if transportation distances are reduced.
Avoiding double handing is essential.
Materials are delivered to site using various methods of packaging.
Some are loose such as sands and gravels. Other materials are in boxes such as tiles and ironmongery. Others are palletted such as bricks and blocks.
Storage may be in huts, a compound either under cover or without cover, or in the building itself.

## Slide 3: Types of Storage
Various materials require different storage:
Loose materials such as sands and gravels require bins to prevent them spreading and being wasted.
Cement requires protection from the weather.
Components such as roof trusses require special attention.
The storage of liquids such as oil and petrol are subject to the following regulations:

## Slide 4: Petrol
Any storage within 6 metres of a building
is governed by the petroleum regulations
and the associated fire regulations.
Where fuel is stored within the building,
containers must have screw tops and not
exceed 9 litres each in capacity, and the maximum number of containers in any store is two.

## Slide 5: Materials
The cost of materials used in the construction industry exceeds 50% of the overall costs.
The site manager has little or no control over the initial price of materials; every contractor has to pay approximately the same price.
However, by employing strict methods of control in handling and using materials the most efficient contractor will involve him/herself in the least cost in their utilization.
In this respect the site supervisor plays a major role.
Effective planning and control procedures instigated by him/herself and management will result in considerable economies.

## Slide 6: Cost of Materials
It is very difficult to state the cost of each material.
This information should be obtained direct from the manufacturer prior to ordering.
The cost of materials can be affected by the amount required – bulk buying can be cheaper.
The distance from the works can cause the cost to rise.

## Slide 7: Quantities of Materials
On smaller contracts the amount of materials required is “taken off” the drawings.
Taking off is the first stage in which the site manager may be involved in material control; company policy will determine who is responsible for taking off.
Whenever possible, taking off should be done directly from the main contract drawings, with cross reference to bills of quantities and specifications.
Any discrepancies, especially those of major consequence, should be reported to the architect as his/her instructions will be required.

## Slide 8: Checking Material Deliveries
This follows taking off.
A list of delivery dates, the amount and sequence the materials will be delivered is produced.
This is called a Materials Delivery Schedule.
A copy of the delivery schedule is held on site together with the “copy orders.”
This allows the site staff to see when materials are due for delivery, allows them to prepare for receipt and to adjust deliveries to suit progress of work.

## Slide 9
WEST BUILDERS LTD MATERIALS DELIVERY SCHEDULE Contract: …………………………………. No:………………………….. Job No: …………………………………. Date: ………………………. Prepared by: ……………………………... |  |  |  | 
Bill reference | Description | Quantities | Delivery dates | Comments

## Slide 10: Material Deliveries
The Material Schedule sheet would have been completed prior to the commencement of the site and gives the site manager the information required for controlling the materials on site.
Where materials arrive on site very early they are more prone to damage or pilfering.

## Slide 11
WEST BUILDERS LTD MATERIALS RECEIVED Contract: …………………………………. Job No: …………………………………. Prepared by: ……………………………... No:………………………….. |  |  |  |  |  | 
Date | Delivery No | Supplier | Materials | Rate | Total value | Comments

## Slide 12: Material Transfers
When materials are required to be transferred between sites correct documentation should be completed.

## Slide 13
WEST BUILDERS LTD MATERIALS RECEIVED No: ……………………… Date: ……………………… |  | 
From site: | To site: | 
Description | Quantity | 
Issued by: | Received by: | Driver’s signature

## Slide 14: Storage for Flammable Items